CITY COLLEGE OF NEW YORK

CSC 34200: COMPUTER ORGANIZATION

PROJECT: Analyzing Performance of Unoptimized Inner Product vs. Optimized Inner Product using Vector Registers

Author:	Supervisor:
Owais Naeem	Professor Izidor Gertner

BACKGROUND

The SIMD (single instruction, multiple data) architecture is modeled after a parallel architecture in which a single instruction can be applied to multiple data objects at a given moment of time. This eliminates the performance overhead of performing instructions sequentially on data objects, one by one. Such an SIMD architecture is enabled by supporting instruction sets, such as SSE (Streaming SIMD Extension), which allow the performing of operations on multiple data objects, or vectors, at a time. Most modern CPUs have support for these instruction sets, and they can be utilized quite effectively to, at time, decrease program run-time by many orders of magnitude.

OBJECTIVE

The objective of this project is to compute the dot product of an array using two different methods, and then compare the performance of the methods to each other. The first method is the general, naïve implementation of computing the dot product, and the second method utilizing is utilizing SSE vector instructions. Analyzing the run-times of both methods will allow us to see just how much more efficient and effective vector instructions can be, when compared with the alternate, general way of performing operations on data.

METHODS

Testing of the vector instructions was conducted on Microsoft Visual C++ 2010 Express on an Intel(R) Code(TM) i5-3337U CPU @1.80 GHz with 4.00GB RAM and 64-bit Windows 7 Home Premium Operating System. The SSE required the inclusion of the xmmintrin.h header file.

DATA AND PROCEDURE

To test the unoptimized dot product and optimized dot product methods, an experiment was setup in Microsoft Visual C++ 2010 Express. The setup of the experiment was as follows:

1. Declare pointers to two arrays to be used as the two 'vectors' to perform the dot product on, and declare an array of varying sizes to be used to allocate the appropriate amount of dynamic memory when testing with arrays of certain sizes. Also, memory was allocated for several pointers that would assist in storing the results of the dot product operations.

2. The declared arrays were filled with ones for example purposes, and to have operations performed on them.

3. The unoptimized version of the dot product was performed on the two arrays, and QueryPerformanceCounter() was used to record how much time elapsed when computing the dot product. This was then output to console for viewing purposes. Refer to Sample 1 in the Appendix for the exact code.

4. The optimized version of the dot product was performed on the two arrays, and QueryPerformanceCounter() was used to record how much time elapsed when computing the dot product. This was then output to the console for viewing purposes. This optimized version of the dot product utilized vector instructions to perform parallel operations on both arrays when loading, multiplying, adding, and storing the contents. Refer to Sample 1 in the Appendix for the exact code.

The following is a brief description of my implementation of the dotProduct_opt() function that utilizes vector instructions can be referred to in Sample 1 of the Appendix, and is also reproduced below:

Several vector registers are declared and initialized with zeros using _mm_setzero_ps().

1. A for loop is used to perform the dot product on the whole array at once.
2. The previously declared vector registers are loaded with the first 12 elements of both arrays, 3 registers for 12 elements of each array using _mm_loadu_ps().

They are then are multiplied component-wise using _ mm_mul_ps(). This multiplies four elements of each array at a time with one call to the _mm_mul_ps() function. Three calls are made so as to multiply four corresponding elements of both arrays, then the next four, and then another four.

Finally, each multiplied component is added together using _mm_add_ps() and stored in *result.

Afterwards, i is incremented by 12 as 12 elements were loaded, multiplied, and added during one run through of the loop.

5. The previous steps were repeated in a loop that kept allocating enough memory for two arrays of a particular array size, filling them up with ones, timing the dot product operations on each when it was being performed, finally outputting to the console, and lastly deallocating the memory allocated for the arrays of a particular size.

6. At the end of the program, there were 18 timing results printed to the console that were ported to MATLAB to represent in a graphical format that clearly presents the difference between the unoptimized and the optimized dot product. Refer to Sample 2 in the Appendix to see the MATLAB program that this data and Figure 2 in the Appendix to see the graph that compares the performance of the unoptimized dot product to the optimized dot product. It is reproduced below for convenience.

CONCLUSION

After writing the C++ code to record the time performance of two different implementations of the dot product of two vectors, one utilizing vector instructions supported by SIMD, and analyzing the outputted results, it can be safely concluded that vector instructions are very effective and efficient. In fact, using them improved the time performance of the dot product operations by orders of magnitude.

Appendix

Sample 1: C++ program that analyzed time performance of unoptimized dot product to optimized dot product:

#include <iostream>
#include <Windows.h>
#include <xmmintrin.h>
#include <iomanip>
using namespace std;

void fill_array(float* a, float* b, int size);
void dotProduct_reg(float* a, float* b, float* result, int size);
void dotProduct_opt(float* a, float* b, float* temp, float* result, int size);

int main()
{
const int sizes = 18;
int size[sizes] = {60, 120, 600, 1200, 6000, 12000, 60000, 120000, 600000, 1200000, 6000000, 12000000, 60000000, 72000000, 84000000, 96000000, 108000000, 120000000};
float *arr1;
float *arr2;
float *result = new float();
float *temp = new float();
__int64 ctr1, ctr2, freq;

for(int i = 0; i < sizes; i++)
{
// initialize
ctr1 = 0, ctr2 = 0, freq = 0;
*result = 0;
const int ARRAY_SIZE = size[i];
arr1 = new float[ARRAY_SIZE];
arr2 = new float[ARRAY_SIZE];

// fill arrays
fill_array(arr1, arr2, ARRAY_SIZE);

// UNOPTIMIZED INNER PRODUCT
cout << "----------" << endl;
if(QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0)
{
dotProduct_reg(arr1, arr2, result, ARRAY_SIZE);
// cout << "(" << i << ")" << " " << "dotProduct_reg() => *result = " << *result << endl; // TO CHECK RESULT
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
cout << "(" << i << ")" << " size = " << setw(8) << size[i] << ", " << "Time (microseconds) for UNOPTIMIZED = " << (((double)(ctr2 - ctr1))/freq)*1000000 << endl;	// in microseconds
}

ctr1 = 0; ctr2 = 0; freq = 0;
*result = 0; *temp = 0;

// OPTIMIZED INNER PRODUCT
if(QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0)
{
dotProduct_opt(arr1, arr2, temp, result, ARRAY_SIZE);
// cout << "(" << i << ")" << " " << "dotProduct_opt() => *result = " << *result << endl; // TO CHECK RESULT
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
cout << "(" << i << ")" << " size = " << setw(8) << size[i] << ", " << "Time (microseconds) for OPTIMIZED = " << (((double)(ctr2 - ctr1))/freq)*1000000 << endl;	// in microseconds
}

delete [] arr1;
delete [] arr2;
}
cout << "----------" << endl;
cin.get();
return 0;
}

void fill_array(float* a, float* b, int size)
{
float *p; float *q;
p = &a[0]; q = &b[0];

// fill with 1s
for(; p < &a[size]; p = p + 1, q = q + 1)
{
*p = 1;
*q = 1;
}
}

void dotProduct_opt(float *a, float *b, float *temp, float* result, int size)
{
__m128 XMM0 = _mm_setzero_ps();
__m128 XMM1 = _mm_setzero_ps();
__m128 XMM2 = _mm_setzero_ps();
__m128 XMM3 = _mm_setzero_ps();
__m128 XMM4 = _mm_setzero_ps();
__m128 XMM5 = _mm_setzero_ps();
__m128 XMM6 = _mm_setzero_ps();
__m128 XMM7 = _mm_setzero_ps();
__m128 XMM8 = _mm_setzero_ps();
__m128 XMMTotal = _mm_setzero_ps();

for(int i = 0; (i+12) <= size; i += 12)
{
XMM0 = _mm_loadu_ps(a + i);
XMM1 = _mm_loadu_ps(a + i + 4);
XMM2 = _mm_loadu_ps(a + i + 8);
XMM3 = _mm_loadu_ps(b + i);
XMM4 = _mm_loadu_ps(b + i + 4);
XMM5 = _mm_loadu_ps(b + i + 8);

XMM6 = _mm_mul_ps(XMM0, XMM3);
XMM7 = _mm_mul_ps(XMM1, XMM4);
XMM8 = _mm_mul_ps(XMM2, XMM5);

XMM0 = _mm_add_ps(XMM6, XMM7);
XMMTotal = _mm_add_ps(XMM0, XMM8);
_mm_storeu_ps(temp, XMMTotal);
*result += (*temp + *(temp+1) + *(temp+2) + *(temp+3));
}
}

void dotProduct_reg(float *a, float *b, float* result, int size)
{
float *p; float *q;
p = &a[0]; q = &b[0];
for(; p < &a[size]; p = p + 1, q = q + 1)
*result += *p * *q;
}

Sample 2: MATLAB code that plots data points representing unoptimized dot product time performance vs. optimized dot product time performance (data points taken from Figure 1 of Appendix):

% Owais Naeem
% Inner Product Project
% Unoptimized vs. Optimized Analysis

x = [60 120 600 1200 6000 12000 60000 120000 600000 1200000 ...
    6000000 12000000 6000000 72000000 84000000 96000000 ...
    108000000 120000000];
y1 = [1.14 2.28 7.41 15.96 75.8282 151.656 775.386 ...
    1534.81 7681.46 16470 76125 153620 766890 924066 1.06534*10^6 ...
    1.22133*10^6 1.36841*10^6 1.53794*10^6];
y2 = [1.14207 1.14207 1.7 4 18 30 96 204 1461 2459 10089 21537 ...
    116924 125854 140120 160060 181162 199886];
plot(x, y1, ':', 'LineWidth', 3);
hold on
plot(x, y2,'--', 'LineWidth', 3);
hold off;
grid
xlabel('Array Size(# of elements)');
ylabel('Time (microseconds)');
title('Unoptimized vs. Optimized Dot Product')
legend('unoptimized', 'optimized')

Figure 1: Output of C++ program referred to in Sample 1 of the Appendix.

Figure 2: MATLAB graph representing unoptimized dot product time performance vs. optimized dot product time performance (graphing data points taken from Figure 1 of Appendix):